## Slide 1
Wedel, 04.06.2025
Sim-To-Real Transfer in RL
Adressing challenges in adapting models trained in simulated environment to the real world.
Art des Dokuments
Notes: [PLACEHOLDER TEXT]

## Slide 2: Titel - Inhalt -
Definition
1.
Observation
2.
Action
3.
Transition
4.
Reward
5.
Outlook
6.

## Slide 3: The overview of Sim-to-Real issue causes.
Source: Da et al., “A Survey of Sim-to-Real Methods in RL: Progress, Prospects and Challenges with Foundation Models”, 2025
Notes: We have the normal RL cycle in the blue box: show the cycle
The Observation Gap ()
is the state of the environment, is the observation based on the state
In simulation the observation is nearly perfectly based on
In reality, the observation is influenced by sensory distortions and differences in the state representation, maybe due to imperfect or impossible measurements
=> So, we have two reason for the gap: differences in sensors and differences in state description
Example: Image in simulation has perfect angle and lightning, the real image has shadows, noise etc.
The Action Gap ()
is the selected action
and are the realized actions in sim or real
The gap depends on differences in the system and the action space (possible actions)
Difference in the system: the action of a robot is moving 5 cm, in sim he moves exact 5 cm, but in real he just moves 3.7 cm due to latency or friction
We can’t model this, because it depends or various reasons: changing over time with an ageing system, mistakes in construction
The Reward Gap ()
: the reward based on an observation and an action
Even if the policy is the same, we’ve different observation and realized actions
Example: in simulation we can get a target distance very easy, in real it’s approximated and can be wrong.
Also, often we assume the same reward function in sim and real. A false reward function in reality can completely devalue the learned behaviour.
The Next State Gap or Transition Gap ()
The transition to a new state depends on a physical model, simulation uses approximations, which doesn’t match the reality.
Probability distributions over state transitions.
Both have same and , but result in different
Very important in physic-based tasks (robotic), not in visual tasks
That is named (used in action- and reward-gap)
The complete gap G of a policy Pi is defined as a performance difference between sim and real, measured with a function Phi. (e.g. the mean reward)
We have the normal RL cycle in the blue box: show the cycle
The Observation Gap (𝑜_𝑡^𝑟𝑒𝑎𝑙≠𝑜_𝑡^𝑠𝑖𝑚)
𝑠_𝑡 is the state of the environment, 𝑜_𝑡 is the observation based on the state
In simulation the observation is nearly perfectly based on 𝒔_𝒕
In reality, the observation is influenced by sensory distortions and differences in the state representation, maybe due to imperfect or impossible measurements
=> So, we have two reason for the gap: ∆𝒑𝒆𝒓𝒄𝒆𝒑𝒕𝒊𝒐𝒏 differences in sensors and ∆𝑺 differences in state description
Example: Image in simulation has perfect angle and lightning, the real image has shadows, noise etc.
The Action Gap (𝑎_𝑡^𝑟𝑒𝑎𝑙≠a_t^sim)
𝑎_𝑡 is the selected action
𝑎_𝑡^𝑠𝑖𝑚 and 𝑎_𝑡^𝑟𝑒𝑎𝑙 are the realized actions in sim or real
The gap depends on differences in the system and the action space (possible actions)
Difference in the system: the action of a robot is moving 5 cm, in sim he moves exact 5 cm, but in real he just moves 3.7 cm due to latency or friction
We can’t model this, because it depends or various reasons: changing over time with an ageing system, mistakes in construction
The Reward Gap (𝑟_𝑡^𝑟𝑒𝑎𝑙≠𝑟_𝑡^𝑠𝑖𝑚)
𝑟_𝑡^𝑠𝑖𝑚≔𝑟(𝑜_𝑡^𝑠𝑖𝑚, 𝑎_𝑡^𝑠𝑖𝑚): the reward based on an observation and an action
Even if the policy is the same, we’ve different observation and realized actions
Example: in simulation we can get a target distance very easy, in real it’s approximated and can be wrong.
Also, often we assume the same reward function in sim and real. A false reward function in reality can completely devalue the learned behaviour.
The Next State Gap or Transition Gap (𝑠_(𝑡+1)^𝑟𝑒𝑎𝑙≠𝑠_(𝑡+1)^𝑠𝑖𝑚)
The transition to a new state depends on a physical model, simulation uses approximations, which doesn’t match the reality.
𝑃_𝑆, 𝑃_𝑅 Probability distributions over state transitions.
Both have same 𝒔_𝒕 and 𝒂_𝒕, but result in different 𝒔_(𝒕+𝟏)
Very important in physic-based tasks (robotic), not in visual tasks
That is named ∆𝑠𝑦𝑠𝑡𝑒𝑚 (used in action- and reward-gap)
The complete gap G of a policy Pi is defined as a performance difference between sim and real, measured with a function Phi. (e.g. the mean reward)

## Slide 4: Measuring the sim-to-real gap.
cloth-sim2real-benchmark

## Slide 5: Observation
Notes: Erwähnen von sensor modeling and augmentation und dem Minitaur Beispiel: They don’t include all available sensor measurements, e.g. the system provides the yaw angle of the base
They exclude it, because the measurement drifts quickly and even a small latency can be totally wrong

## Slide 6: Domain Randomization
Modified from: Tobin et al., “Domain Randomization for Transferring Deep Neural Networks from Simulation to the Real World”, IROS, 2017
Source: GitHub, 2025, https://github.com/google-deepmind/mujoco
…
Train
Test
Average detection error on geometric shapes by method, cm |  |  | 
Evaluation type | Real images |  | 
 | Object only | Distractors | Occlusions
Full method | 1.3 ± 0.6 | 1.8 ± 1.7 | 2.4 ± 3.0
No noise added | 1.4 ± 0.7 | 1.9 ± 2.0 | 2.4 ± 2.8
No camera randomization | 2.0 ± 2.1 | 2.4 ± 2.3 | 2.9 ± 3.5
No distractors in training | 1.5 ± 0.6 | 7.2 ± 4.5 | 7.4 ± 5.3
Source: Tobin et al., “Domain Randomization for Transferring Deep Neural Networks from Simulation to the Real World”, IROS, 2017
Notes: 1703.06907
We randomize the following aspects of the domain for each sample used during training:
Number and shape of distractor objects on the table, between 0-10 distractor objects
Position and texture of all objects on the table
Textures of the table, floor, skybox, and robot
Position, orientation, and field of view of the camera
Number of lights in the scene
Position, orientation, and specular characteristics of the lights
Type and amount of random noise added to images
Random textures:
A random RGB value
A gradient between two random RGB values
A checker pattern between two random RGB values
Rendering in MuJoCo Engine, physic engine from Google DeepMind
Trained object detectors for each geometric object with 20,000 training examples
Evaluation on 480 real images with varying distance and distractor objects

## Slide 7: Domain Randomization
Source Domain Extracted Feature
Target Domain Extracted Feature
Randomized Data Distribution
Modified from: Zhao et al., “Sim-to-Real Transfer in Deep Reinforcement Learning for Robotics: a Survey”, IEEE, 2020
Notes: Performing randomization directly on the input of a learning algorithm makes the task potentially harder than necessary.
The algorithm has to model both the arbitrary changes in the visual domain, while at the same time trying to decipher the dynamics of the task.

## Slide 8: Domain Adaptation
Domain Adaptation
Source Domain
Target Domain
Feature Extraction
Feature Extraction
Source Domain Extracted Feature
Target Domain Extracted Feature
Source Domain Feature Space
Target Domain Feature Space
Unified Feature Space
Modified from: Zhao et al., “Sim-to-Real Transfer in Deep Reinforcement Learning for Robotics: a Survey”, IEEE, 2020
Notes: Exceptionally challenging problem: successfully pick up previously unseen objects
Memorize Grasps work well for individual instances, but we need an internal understanding of geometry and physics
Sim-to-Real challenge is particularly difficult: besides the distributional shift from simulated images and physics, the system must also handle domain shift in the distribution of objects themselves

## Slide 9: Robotic grasping with CycleGAN.
Simulation-to-Real Model | Robot Grap Success after 580,000 real episodes
Sim-Only | 21%
Randomized Sim | 37%
RL-CycleGAN | 70%
Modified from: Rao et al., “RL-CycleGAN: Reinforcement Learning Aware Simulation-To-Real”, IEEE, 2020
Notes: Exceptionally challenging problem: successfully pick up previously unseen objects
Memorize Grasps work well for individual instances, but we need an internal understanding of geometry and physics
Sim-to-Real challenge is particularly difficult: besides the distributional shift from simulated images and physics, the system must also handle domain shift in the distribution of objects themselves
In fact, we have two generators: The first tries to map X to Y, the other tries the opposite.
The CycleGAN further imposes a cycle consistency loss, to encourage x → G(x) → F(G(x)) ≈ x and y → F(y) → G(F(y)) ≈ y.

## Slide 10: RL-CycleGAN
Modified from: Rao et al., “RL-CycleGAN: Reinforcement Learning Aware Simulation-To-Real”, IEEE, 2020
Notes: Training of the generators
We train two q-learning functions
We calculate the predictions
We calculate a distance between every predicted q-value, that‘s our loss, we penalize changes in the q-values
We optimize F and G
We don‘t focus on the quality of the predicted actions, we just want to avoid different predictions for the modified images, a sign that the generator isn‘t perfect
Finally we train a final q-learning function

## Slide 11: Fazit zu Oberservation

## Slide 12: Überschrift: maximal 2 Zeilen
Wer?
Wo?
Wann?
Wie?
Timing
Jan
Dez
A
B
C
Wieviel?
Visualisierung
Text
ABC
XYZ
Untertitel – Arial 14pt Fett
Zweiter Untertitel – Arial 12pt
STICKER
1) Zwei Leerzeichen
Anm.: Zwei Leerzeichen
Quelle: Zwei Leerzeichen

## Slide 13: Überschrift: maximal 2 Zeilen
Untertitel – Arial 14pt Fett
Zweiter Untertitel – Arial 12pt
1) Zwei Leerzeichen
Anm.: Zwei Leerzeichen
Quelle: Zwei Leerzeichen
Text
TEXT
  Text
  Text
TEXT
  Text
  Text
TEXT
  Text
  Text
Low
High
Label
Low
High
Label
12pt Text
12pt Text
12pt Text
12pt Text
STICKER

## Slide 14: Diese Sticker und Formen sollten verwendet werden
BACKUP
CONFIDENTIAL
DRAFT
FOR DISCUSSION
EXAMPLE
ILLUSTRATIVE
PRELIMINARY
ANHANG
VERTRAULICH
ENTWURF
ZUR DISKUSSION
BEISPIEL
ILLUSTRATIV
VORLÄUFIG
KONZEPTIONELL
CONCEPTIONAL
Insert Text Here
Insert Text Here
Text
Text attached to cloud
hoch
niedrig
#
#
Bullet A
Bullet B
Bullet C
Bullet D
FINAL
FINAL
Sticker und Formen

## Slide 15: - BACKUP -
Titel