## Slide 1
Wedel, 04.06.2025
Sim-To-Real Transfer in RL
Adressing challenges in adapting models trained in simulated environment to the real world.
Notes: [PLACEHOLDER TEXT]

## Slide 2: Titel - Inhalt -
Definition
1.
Observation
2.
Action
3.
Transition
4.
Reward
5.
Outlook
6.

## Slide 3: DL is data hungry, but Robotic Data is expensive.
Robot Cost
Security
Labeling
Notes: Labeling is the process to get annotations for the model like robot interactions, sensor data, images etc.
This is why we use simulation

## Slide 4: The Use of a Simulation leads to The Edge Case Problem.
https://x.com/hfxtraffic/status/1799443590868779498
https://en.wikipedia.org/wiki/Interchange_%28road%29
http://www.whitewolfpack.com/2015/04/genius-elephant-stops-traffic-so-little.html
Notes: How can we make our system robust to them?

## Slide 5: The overview of Sim-to-Real issue causes.
Source: Da et al., “A Survey of Sim-to-Real Methods in RL: Progress, Prospects and Challenges with Foundation Models”, 2025
Notes: We have the normal RL cycle in the blue box: show the cycle
The Observation Gap ()
is the state of the environment, is the observation based on the state
In simulation the observation is nearly perfectly based on
In reality, the observation is influenced by sensory distortions and differences in the state representation, maybe due to imperfect or impossible measurements
=> So, we have two reason for the gap: differences in sensors and differences in state description
Example: Image in simulation has perfect angle and lightning, the real image has shadows, noise etc.
The Action Gap ()
is the selected action
and are the realized actions in sim or real
The gap depends on differences in the system and the action space (possible actions)
Difference in the system: the action of a robot is moving 5 cm, in sim he moves exact 5 cm, but in real he just moves 3.7 cm due to latency or friction
We can’t model this, because it depends or various reasons: changing over time with an ageing system, mistakes in construction
The Reward Gap ()
: the reward based on an observation and an action
Even if the policy is the same, we’ve different observation and realized actions
Example: in simulation we can get a target distance very easy, in real it’s approximated and can be wrong.
Also, often we assume the same reward function in sim and real. A false reward function in reality can completely devalue the learned behaviour.
The Next State Gap or Transition Gap ()
The transition to a new state depends on a physical model, simulation uses approximations, which doesn’t match the reality.
Probability distributions over state transitions.
Both have same and , but result in different
Very important in physic-based tasks (robotic), not in visual tasks
That is named (used in action- and reward-gap)
The complete gap G of a policy Pi is defined as a performance difference between sim and real, measured with a function Phi. (e.g. the mean reward)
We have the normal RL cycle in the blue box: show the cycle
The Observation Gap (𝑜_𝑡^𝑟𝑒𝑎𝑙≠𝑜_𝑡^𝑠𝑖𝑚)
𝑠_𝑡 is the state of the environment, 𝑜_𝑡 is the observation based on the state
In simulation the observation is nearly perfectly based on 𝒔_𝒕
In reality, the observation is influenced by sensory distortions and differences in the state representation, maybe due to imperfect or impossible measurements
=> So, we have two reason for the gap: ∆𝒑𝒆𝒓𝒄𝒆𝒑𝒕𝒊𝒐𝒏 differences in sensors and ∆𝑺 differences in state description
Example: Image in simulation has perfect angle and lightning, the real image has shadows, noise etc.
The Action Gap (𝑎_𝑡^𝑟𝑒𝑎𝑙≠a_t^sim)
𝑎_𝑡 is the selected action
𝑎_𝑡^𝑠𝑖𝑚 and 𝑎_𝑡^𝑟𝑒𝑎𝑙 are the realized actions in sim or real
The gap depends on differences in the system and the action space (possible actions)
Difference in the system: the action of a robot is moving 5 cm, in sim he moves exact 5 cm, but in real he just moves 3.7 cm due to latency or friction
We can’t model this, because it depends or various reasons: changing over time with an ageing system, mistakes in construction
The Reward Gap (𝑟_𝑡^𝑟𝑒𝑎𝑙≠𝑟_𝑡^𝑠𝑖𝑚)
𝑟_𝑡^𝑠𝑖𝑚≔𝑟(𝑜_𝑡^𝑠𝑖𝑚, 𝑎_𝑡^𝑠𝑖𝑚): the reward based on an observation and an action
Even if the policy is the same, we’ve different observation and realized actions
Example: in simulation we can get a target distance very easy, in real it’s approximated and can be wrong.
Also, often we assume the same reward function in sim and real. A false reward function in reality can completely devalue the learned behaviour.
The Next State Gap or Transition Gap (𝑠_(𝑡+1)^𝑟𝑒𝑎𝑙≠𝑠_(𝑡+1)^𝑠𝑖𝑚)
The transition to a new state depends on a physical model, simulation uses approximations, which doesn’t match the reality.
𝑃_𝑆, 𝑃_𝑅 Probability distributions over state transitions.
Both have same 𝒔_𝒕 and 𝒂_𝒕, but result in different 𝒔_(𝒕+𝟏)
Very important in physic-based tasks (robotic), not in visual tasks
That is named ∆𝑠𝑦𝑠𝑡𝑒𝑚 (used in action- and reward-gap)
The complete gap G of a policy Pi is defined as a performance difference between sim and real, measured with a function Phi. (e.g. the mean reward)

## Slide 6: Measuring the sim-to-real gap.
Source: Mulero et al., “Benchmarking the Sim-to-Real Gap in Cloth Manipulation”, IEEE, 2981-2988 (2024)
Notes: Chequered Rag = Karo-Lappen
Towel Rag = Handtuch-Lappen
Linen Rag = Leinen-Lappen
See Towels and actions on them
Dynamic is swinging
Quasi-static is hanging and letting down slowly
We have real observations and imitation of the simulator
The distance is measured
This is without any RL model and we already have a gap
Even in (quasi-)static tasks

## Slide 7: Attention to impossible or difficult measurements in reality.
„Note that we do not include all available sensor measurements in the observation space. For example, the IMU also provides the yaw of the base. We exclude it because the measurement drifts quickly.“
Source: Tan et al., “Sim-to-real: Learning agile locomotion for quadruped robots”, arXiv preprint arXiv: 1804.10332 (2018)
Notes: This slide is based on the work by Tan et al. (2018) titled "Sim-to-Real: Learning Agile Locomotion for Quadruped Robots."
In the paper, the authors use deep reinforcement learning to train locomotion policies for a quadruped robot – specifically for galloping and trotting gaits.
Training is performed entirely in simulation, and the learned policy is then deployed directly to a real-world robot — the Ghost Robotics Minitaur — without additional fine-tuning.
The main challenge is the Sim-to-Real gap: simulation and the real world differ in many small but critical ways — for example, in actuator behavior, sensor noise, or latency.
To minimize this gap, the authors improve simulation fidelity and make the learned policies more robust, e.g. by adding noise, latency modeling, and system identification.
One subtle but important design decision: They exclude the yaw angle (rotation around the Z-axis) from the observation space.
Why? Because the IMU yaw measurement drifts significantly over time in the real robot. Including it would mean the agent learns to rely on a signal that's unreliable in deployment — leading to failure.
This is a key takeaway: Sim-to-Real transfer starts with designing your observation space based on what you can actually trust in the real world.
So in simulation, we shouldn’t blindly use all available sensor data — we must consider what is feasible and stable to measure in reality.

## Slide 8: Domain Randomization
Modified from: Tobin et al., “Domain Randomization for Transferring Deep Neural Networks from Simulation to the Real World”, IROS, 2017
Source: GitHub, 2025, https://github.com/google-deepmind/mujoco
…
Train
Test
Average detection error on geometric shapes by method, cm |  |  | 
Evaluation type | Real images |  | 
 | Object only | Distractors | Occlusions
Full method | 1.3 ± 0.6 | 1.8 ± 1.7 | 2.4 ± 3.0
No noise added | 1.4 ± 0.7 | 1.9 ± 2.0 | 2.4 ± 2.8
No camera randomization | 2.0 ± 2.1 | 2.4 ± 2.3 | 2.9 ± 3.5
No distractors in training | 1.5 ± 0.6 | 7.2 ± 4.5 | 7.4 ± 5.3
Source: Tobin et al., “Domain Randomization for Transferring Deep Neural Networks from Simulation to the Real World”, IROS, 2017
Notes: We randomize the following aspects of the domain for each sample used during training:
Number and shape of distractor objects on the table, between 0-10 distractor objects
Position and texture of all objects on the table
Textures of the table, floor, skybox, and robot
Position, orientation, and field of view of the camera
Number of lights in the scene
Position, orientation, and specular characteristics of the lights
Type and amount of random noise added to images
Random textures:
A random RGB value
A gradient between two random RGB values
A checker pattern between two random RGB values
Rendering in MuJoCo Engine, physic engine from Google DeepMind
Trained object detectors for each geometric object with 20,000 training examples
Evaluation on 480 real images with varying distance and distractor objects

## Slide 9: Domain Randomization
Source Domain Extracted Feature
Target Domain Extracted Feature
Randomized Data Distribution
Modified from: Zhao et al., “Sim-to-Real Transfer in Deep Reinforcement Learning for Robotics: a Survey”, IEEE, 2020
Notes: Performing randomization directly on the input of a learning algorithm makes the task potentially harder than necessary.
The algorithm has to model both the arbitrary changes in the visual domain, while at the same time trying to decipher the dynamics of the task.

## Slide 10: Domain Adaptation
Domain Adaptation
Source Domain
Target Domain
Feature Extraction
Feature Extraction
Source Domain Extracted Feature
Target Domain Extracted Feature
Source Domain Feature Space
Target Domain Feature Space
Unified Feature Space
Modified from: Zhao et al., “Sim-to-Real Transfer in Deep Reinforcement Learning for Robotics: a Survey”, IEEE, 2020
Notes: Exceptionally challenging problem: successfully pick up previously unseen objects
Memorize Grasps work well for individual instances, but we need an internal understanding of geometry and physics
Sim-to-Real challenge is particularly difficult: besides the distributional shift from simulated images and physics, the system must also handle domain shift in the distribution of objects themselves

## Slide 11: Robotic grasping with CycleGAN.
Simulation-to-Real Model | Robot Grap Success after 580,000 real episodes
Sim-Only | 21%
Randomized Sim | 37%
RL-CycleGAN | 70%
Modified from: Rao et al., “RL-CycleGAN: Reinforcement Learning Aware Simulation-To-Real”, IEEE, 2020
Notes: Exceptionally challenging problem: successfully pick up previously unseen objects
Memorize Grasps work well for individual instances, but we need an internal understanding of geometry and physics
Sim-to-Real challenge is particularly difficult: besides the distributional shift from simulated images and physics, the system must also handle domain shift in the distribution of objects themselves
In fact, we have two generators: The first tries to map X to Y, the other tries the opposite.
The CycleGAN further imposes a cycle consistency loss, to encourage x → G(x) → F(G(x)) ≈ x and y → F(y) → G(F(y)) ≈ y.

## Slide 12: RL-CycleGAN
Modified from: Rao et al., “RL-CycleGAN: Reinforcement Learning Aware Simulation-To-Real”, IEEE, 2020
Notes: Training of the generators
We train two q-learning functions
We calculate the predictions
We calculate a distance between every predicted q-value, that‘s our loss, we penalize changes in the q-values
We optimize F and G
We don‘t focus on the quality of the predicted actions, we just want to avoid different predictions for the modified images, a sign that the generator isn‘t perfect
Finally we train a final q-learning function

## Slide 13: Fazit zu Oberservation
TODO: ensemble, when (not) to use

## Slide 14: Action-Level Transfer
TODO: evaluation
Source: Tan et al., “Sim-to-Real: Learning Agile Locomotion For Quadruped Robots”, arXiv: 1804.10332, 2018
Notes: Another example: Minitaur robot, is a robot for legged locomotion
We’ve a real-time simulation and latency in the real
We track the last episodes and model the latency, but this isn’t completely safe (show small outlier in the graph)
So, additional we use randomization, we add a random value in the range on the right table.
Like Observation-Level-Transfer, but with action-related parameters
Fade in: The blue parameters are directly action-related, the red are observation-related, the other influence the action indirect
Explanation: mass: Trägheit, influenced moving results after an action
inertia: How hard a body changes its rotation - affects the action result.
Contact friction: Interacts with soil reaction after action → slippage etc.
Battery voltage: Influence engine power
IMU: the engine which is reading the sensor data

## Slide 15: Grounded Action Transformation
Source: Hanna et al., “Grounded action transformation for sim-to-real reinforcement learning”, Mach Learn 110, 2469-2499 (2021)
GSL
GAT
Notes: In GSL the parameters in the policy are changed after real-world feedback. Compare to hyperparameter tuning
Problem: changes in the simulator, expert knowledge, flexible just on parametric level, doesn’t work with all simulators

## Slide 16: Grounded Action Transformation
Source: Hanna et al., “Grounded action transformation for sim-to-real reinforcement learning”, Mach Learn 110, 2469-2499 (2021)
Chart: 
| θ_0 | GUIDED GSL | GAT SimSpark | GAT Gazebo
Velocity (cm/s) | 19.52 | 24.59 | 27.97 | 26.89
% Improve | 0 | 25.9734 | 43.2889 | 37.7561
The walking speed for GUIDED GSL was estimated by applying the reported improvement of 26% (as cited in Hanna & Stone, 2017) to the baseline speed of the initial policy (θ₀ = 19.52 cm/s). While the original GSL study used a different setup, this extrapolated value is included for illustrative comparison only.
TODO: when (not) to use
Notes: In GSL the parameters in the policy are changed after real-world feedback.
Problem: changeable parameters (not everything is changeable), GSL needs expert knowledge, GAT is data-driven, GAT is lightweight, no change of the simulator
Disadvantages of GAT:
For all (s_t, a_t, s_t+1) observed in the real world, there exist a a transformed function à_t that produces s_t+1 in the simulator: e.g. contact dynamics or unmodeled environmental influences, non-linear systems with delays
The training data comes from the trajectory distribution of θ₀, the model just learn actions and states, that occur frequently in θ₀, in the training the policy sees other states, the new states lie outside the training distribution of f and f-¹ₛᵢₘ.
Solution: Dataset Aggregation (DAgger)
GAT just fits the actions not the observations
GAT does not take explicit latencies into account
Conclusion:
Currently not used in production
Possible usable in security critic domain
Whats missing for production?
  Online-adaptation
  Observation-grounding
  Performance guarantees

## Slide 17: Robust Policy Design
TODO: add content

## Slide 18: System Identification (SysID)
TODO: add content
Notes: Transition from domain randomization
Randomization has limits: if the real-world dynamics lie outside the randomized range, or if the gap is irreducible, e.g. complex contact physics that simulators cannot represent
Randomization offers little guidance for refining the sim parameters post-transfer (offers no ideas for improvement of the parameters)
So we use System Identification: using real-world data to calibrate the simulator
Early efford looked at the real-world and manual tuned the physical parameters
Newer approaches automated it

## Slide 19: Simulation Optimization
Source Mean
Target Mean
Modified from: Chebotar et al., “Closing the Sim-to-Real Loop: Adapting Simulation Randomization with Real World Experience”, ICRA, 8973-8979 (2019)
Notes: Goal: Match simulated behavior to real-world behavior by adjusting the distribution over simulation parameters.
Start with initial distribution: mulitvariate Gaussian over simulation parameters, e.g. friction, mass, joint damping, object position
Train policy in simulation: samples simulation parameters, learns policy under diverse simulated scenarios
Collect real-world rollouts: Execute policy to real robot, record the observation tracetories
Compute discrepancy: Compare real and simulated observations using a distance metric
Update simulation distribution: Minimize the expected discrepancy
Repeat: alternate between training and distribution update
Why not for Domain Randomization?
No real data, overfitting, not all parameters identificable, different target: DR -> robustness, SimOpt -> precision in a known env
Why not for Observation or Action?
Observation error are non-linear and high-dimensional, no feedback
Action is also for other for other tasks, e.g. scaling, bias, discrete vs. continuous
But is theoretical possible, needs exact modeling, much data, complex feedback

## Slide 20: Evaluation
https://www.youtube.com/watch?v=nilcJY5Kdt8
Source: Chebotar et al., “Closing the Sim-to-Real Loop: Adapting Simulation Randomization with Real World Experience”, ICRA, 8973-8979 (2019)
Notes: Ab Sekunde 51
Left: SimOpt adjusts physical parameter distribution of the soft rope, peg and the robot, which results in a successful execution of the task on a real robot after two SimOpt iterations.
Right: SimOpt adjusts physical parameter distribution of the robot and the drawer. Before updating the parameters, the robot pushes too much on the drawer handle with one of its fingers, which leads to opening the gripper. After one SimOpt iteration, the robot can better control its gripper orientation, which leads to an accurate task execution.

## Slide 21: Learned Reward Functions
Notes: Why Use Reward-Based Techniques in Sim-to-Real Transfer?
Simulation Rewards Are Often Unrealistic In simulation, we have full access to ground-truth states (e.g., object positions, velocities). Real robots don’t have perfect state access — rewards based on idealized data lead to poor real-world generalization.
Overfitting to Artificial Reward Signals Simulated rewards may be dense, precise, and idealized. This encourages behaviors that exploit simulation-specific shortcuts, not strategies that work in reality.
Mismatch Between Sim and Real Reward Availability The way rewards are computed in sim (e.g., using internal simulator data) is not replicable in the real world. If the agent relies on those reward structures, it won’t behave meaningfully once deployed.
Reward Shapes the Exploration Space Rewards guide what parts of the environment the agent explores during training. Poor reward shaping leads to insufficient exposure to realistic situations.
Sparse or Learned Rewards Improve Robustness Using sparse, goal-based, or learned rewards can make the policy more general and less reliant on specific sim conditions. Techniques like adversarial imitation learning or reward modeling from real demonstrations align training more closely with real-world success.

## Slide 22: Inverse Reinforcement Learning
Source: Ng et al., “Algorithms for Inverse Reinforcement Learning”, ICML, 663-670 (2000)
Notes: Normal: Learn a reward function from a given policy
Now: Learn a reward function from real observations, to use this in the simulation
Problem: We doesn’t have a perfect policy, so our reward modelling must be robust against imperfect samples

## Slide 23: Adversarial IRL
Policy
Discriminator
Discriminator Score
Reward Function
Real Trajectories
Used for training
Notes: We train a policy which tries to imitate the real observations. The real and simulated trajectories are rated from a discriminator how real they seem
This creates the reward.
Based on the reward we optimize the policy.
With the policy we can discover more examples of the environment, which helps against overfitting and local maximum
This reward formula combines two goals:
Imitation via 𝑓(𝑠,𝑎)
f(s,a)):The reward is high if the action looks as if it comes from an expert (discriminator says “good”).
Exploration / regularization via -log𝜋(𝑎∣𝑠)
-logπ(a∣s)):Punishes deterministic policies → promotes stochastic behavior. Prevents the policy from becoming too rigidly focused on individual actions, which can happen with overadjusted (overfitting) rewards.
Why AIRL is robust to imperfect outliers?
Adversarial framing: AIRL doesn't require demonstrations to be strictly optimal — it learns to distinguish expert-like behavior statistically rather than assuming perfection.
Discriminator learns distributions: Instead of binary classification, the discriminator outputs probabilities. Outlier actions simply receive lower confidence, not hard rejection.
Maximum Entropy regularization: The reward is defined as r(s,a)=f(s,a)−log⁡π(a∣s)r(s, a) = f(s, a) - \log \pi(a|s)r(s,a)=f(s,a)−logπ(a∣s) → This penalizes overconfident (deterministic) policies and promotes diverse, exploratory behavior — which helps smooth over noisy or inconsistent expert data.
Implicit robustness to noise: Imperfect or inconsistent samples don't dominate training, because the discriminator sees them as low-probability samples rather than rejecting the entire trajectory.
Focus on general trends, not individual errors: AIRL captures global patterns of expert behavior. Outliers affect the reward function only locally, not systematically.
Reward learned as a scoring function, not a strict imitation signal: AIRL optimizes a reward model that gradually separates “likely expert” from “unlikely expert” behavior — making it more tolerant of variance in the data.

## Slide 24: Preference-based RL (PbRL) is used to determine an unknown reward function.
Policy
Environment
action
state
reward
state
Preference
Notes: Trajectory Generation The policy π\piπ interacts with a simulated environment to generate trajectories τ\tauτ, i.e. sequences of state–action pairs ((o0,a0),(o1,a1),…,(oT,aT))((o_0, a_0), (o_1, a_1), \dots, (o_T, a_T))((o0​,a0​),(o1​,a1​),…,(oT​,aT​)). These trajectories are collected without requiring access to a predefined reward function.
Reward from Human Preference Instead of using an environment-defined reward, human feedback is used to define rewards indirectly. A human compares pairs of trajectory segments and selects the preferred one. This creates binary or ranked preference data over behavior rather than scalar rewards.
Reward Model Learning A neural network learns to approximate a latent reward function r^\hat{r}r^ that explains the human's preferences. The network is updated using supervised learning from these comparisons.
Policy Optimization The learned reward signal r^\hat{r}r^ is then used to train the policy π\piπ using a standard RL algorithm (e.g. TRPO, PPO). The feedback loop continues: as the policy improves, new trajectories are generated and queried.
🛠️Relevance for Sim-to-Real Transfer
Simulation as a Safe Training Ground The agent is trained in simulation, avoiding the risks and costs of real-world experimentation.
No Handcrafted Rewards Needed Preference-based feedback bypasses the need for accurate or safe reward specification in the real world.
Aligning with Human Intentions Human feedback captures qualitative goals (e.g. smoothness, safety, style) that are hard to express mathematically.
Bridging the Reality Gap Because preferences reflect real-world goals rather than simulated metrics, the trained behavior generalizes better to real deployments.

## Slide 25: Preference-based RL can imitate the perfect reward function with just a few interactions.
Source: Christiano et al., “Deep Reinforcement Learning from Human Preferences”, NIPS, (2017)
Notes: We see the average reward over 5 batches, with different reward functions: once is with the real reward function, the other with feedback queries.
Synthetic queries are not generated by humans, they are generated with the real reward function
We can see that policy with feedback perform often near or as good as the real reward function.
All tasks in simulation, no sim-to-real
Relevant to sim2real bc:
We doesn’t need a predefined reward function
Real world rw func are too complex

## Slide 26: … even in real Applications.
Metric | FLoRA | Fine-Tune
Success Rate (%) | 65 | 10
Near Collision Rate (%) | 10 | 20
Average Finish Distance (m) | 0.59 | 0.61
Metric | FLoRA | Fine-Tune
Distance Pushed (cm) | 65 | 10
Velocity () | 10 | 20
Metric | FLoRA | Fine-Tune
Distance Pushed (cm) | 65 | 10
 | 10 | 20
Modified from: Marta et al., “FLoRA: Sample-Efficient Preference-based RL via Low-Rank Style Adaptation of Reward Functions”, (2025)
Notes: FLoRA is an ensemble method which pre-train a policy with a basic reward function and fine-tune with PbRL
The basic reward function is task specific, but not fine-tuned
Measuring the sim-to-real gap is hard, bc we always can use a bad reward function

## Slide 27: PbRL adjusts the reward in detail and precisely.
a) Original Reward
c) FLoRA
b) Fine - Tune
Modified from: Marta et al., “FLoRA: Sample-Efficient Preference-based RL via Low-Rank Style Adaptation of Reward Functions”, (2025)
Notes: We see dim reduced state-action-pairs and the reward
Before just like -5 and +1
Now flexible and very detailed values for each pair
Reduced with t-SNE

## Slide 28: Case Study
TODO: ADR

## Slide 29: Überschrift: maximal 2 Zeilen
Wer?
Wo?
Wann?
Wie?
Timing
Jan
Dez
A
B
C
Wieviel?
Visualisierung
Text
ABC
XYZ
Untertitel – Arial 14pt Fett
Zweiter Untertitel – Arial 12pt
STICKER
1) Zwei Leerzeichen
Anm.: Zwei Leerzeichen
Quelle: Zwei Leerzeichen

## Slide 30: Überschrift: maximal 2 Zeilen
Untertitel – Arial 14pt Fett
Zweiter Untertitel – Arial 12pt
1) Zwei Leerzeichen
Anm.: Zwei Leerzeichen
Quelle: Zwei Leerzeichen
Text
TEXT
  Text
  Text
TEXT
  Text
  Text
TEXT
  Text
  Text
Low
High
Label
Low
High
Label
12pt Text
12pt Text
12pt Text
12pt Text
STICKER

## Slide 31: Diese Sticker und Formen sollten verwendet werden
BACKUP
CONFIDENTIAL
DRAFT
FOR DISCUSSION
EXAMPLE
ILLUSTRATIVE
PRELIMINARY
ANHANG
VERTRAULICH
ENTWURF
ZUR DISKUSSION
BEISPIEL
ILLUSTRATIV
VORLÄUFIG
KONZEPTIONELL
CONCEPTIONAL
Insert Text Here
Insert Text Here
Text
Text attached to cloud
hoch
niedrig
#
#
Bullet A
Bullet B
Bullet C
Bullet D
FINAL
FINAL
Sticker und Formen

## Slide 32: - BACKUP -
Titel